## Slide 1
Power – Up sequence
  Whenever power cycle happens the device (COPLA) will compare the header of existing profile.zlb with the profile.zlb file of host (M168).
  If both the headers are different, then download new profile.zlb to the flash otherwise it will not get downloaded.
  Calculate CRC on profile.bin if exists and Compare with CRC at profile.zlb header
  If both CRC are not same or no profile.bin, unzip the profile.zlb to profile.bin
  Else use the existing profile.bin
Profile handler in existing BACW module

## Slide 2
New requirment
  Data MUST persistance after device power cycle
  User can modify the object using BACnet Client
  User changes only overwritten in the case of new profile.zlb in any other cases changes MUST be there
Profile Handler Modification for Schedular and Calender Object

## Slide 3
  Approach 1st
    Create a copy of Schedular and Calender object to avoid the CRC change in profile.bin after object modification by the BACnet Client.
  Approach 2nd
    Profile.zlb should not be unzip until new profile.zlb available at M168. Allow user to modify the profile.bin
Profile handler for New solution

## Slide 4
Keeping a seperate copy of calendar and schedule objects in the flash section. Application will access for data from this section rather than accessing from profile.bin file.
If the user wants to modify the property values , can do in this section without modifying the profile.bin directly.
New section as well need to replace wrt profile.zlb in case of new profile.zlb coming from M168
Advantages:
No CRC mismatch between profile.zlb and profile.bin
Limitations:
The copy of the calendar and schedule objects consumes extra memory .
The object size for schedule object is comparitively big and hence it will not support more schedule objects.
Approach 1st

## Slide 5
Allow user to Modify the profile.bin for schedular and calender object.
Calculate CRC after each modification, to verify profile.bin consistancy at every power cycle
Do not compare CRC of profile.bin with profile.zlb, instead compare with modified CRC.
Advantage:
There will no extra memory required for Calender and Schedular object.
Limitation:
There will be CRC mismatch between profile.zlb and profile.bin and need to take care in new design
Approach 2nd

## Slide 6
Host(M168) contains the new profile.zlb file
Host contains old profile.zlb file and device contains old profile.bin file
Host contains old profile.zlb file and device contains modified profile.bin file
Use case address with New Design by considuring Approach-2

## Slide 7
Host(M168) contains the new profile.zlb file
Device will compare the Profile.zlb Header with the Header of same file of the Host.
If the headers are not same , download profile.zlb file from the host and replace it with the existing file.
Unzip the the profile.zlb file to profile.bin file
Check the CRC of the profile.bin file, if CRC is ok then go for object initialization.
Put the profile CRC at separate location, Next power cycle onward device will use this CRC to verfy wrt profile.bin CRC . Till new profile.zlb available at M168
Use Case -1

## Slide 8
Host contains old profile.zlb file and device contains old profile.bin file
Device will compare the Profile.zlb Header with the Header of same file on the Host.
Since both the header are same, device will bypass the profile.zlb download .
Device will calculate CRC for profile.bin and compare wrt to modified CRC instead of profile Header CRC.
If the CRC passed, then device will going to initilize the objects from flash.
Use Case -2

## Slide 9
Host contains old profile.zlb and modified profile.bin file
Device will compare the Profile.zlb Header with the Header of same file on the Host.
Since both the header are same, device will bypass the profile.zlb download .
Device caldulate CRC over profile.bin and compare with new CRC which is caluated after profile.bin modification.
If CRC matches device will contineue with existing profile.bin
Else unzip the profile.zlb and overwrite the profile.bin (in case of profile.bin currupted)
Use Case -3